## Slide 1
A Division of Wi-LAN Inc.
www.tiltek.com
Affordable Quality
Broadband Wireless World Forum
February 12 – 14, 2002
David Tilston
Strategies for Reducing Interference by Effectively Evaluating and Deploying Directional Antennas

## Slide 2
A Division of Wi-LAN Inc.
www.tiltek.com
ISO 9001:94 Certified
Sources and Types of Interference
Co-channel interference
  Originating from “co-located” antennas/systems sharing the same channel.
Adjacent channel interference
  Originating from “co-located” antennas/systems or from nearby base-station sites on an adjacent channel.
Noise and other sources of interference and distortion
  Uncorrelated noise (e.g. other wireless services, WAN/LAN systems, microwave ovens, etc.).
  Delay distortion (due to reflected paths, etc).
  Solar/thermal noise.

## Slide 3
A Division of Wi-LAN Inc.
www.tiltek.com
Solutions That Work
Typical Point-to-Multipoint System
CPE Sites
Interfering Site
Interfering Site
AP Site

## Slide 4
A Division of Wi-LAN Inc.
www.tiltek.com
Affordable Quality
Multiple Point-to-Multipoint Systems

## Slide 5
A Division of Wi-LAN Inc.
www.tiltek.com
ISO 9001:94 Certified
Path Lengths and Path Loss

## Slide 6
A Division of Wi-LAN Inc.
www.tiltek.com
ISO 9001:94 Certified
Path Lengths and Path Loss

## Slide 7
A Division of Wi-LAN Inc.
www.tiltek.com
Outstanding Reliability
Interference Calculations
Overview
  We will analyze the system configuration at 2.4 GHz.
  In all cases we will assume the same Tx power, cable losses, antenna heights Rx Sensitivity as follows:
    Tx Power: +20 dBm.
    Rx Sensitivity: -81 dBm.
    AP Antenna Height: 50 m (164 ft.).
    Cable at AP: 50 m, LMR-600.
    CPE Antenna Height: 10 m (33 ft.).
    Cable at CPE: 10 m, LMR-400.
    Line of Sight (LOS) paths with adequate Fresnel zone clearance (i.e. approx. 0.6 F1 minimum).

## Slide 8
A Division of Wi-LAN Inc.
www.tiltek.com
Outstanding Reliability
Link Calculation Worksheet

## Slide 9
A Division of Wi-LAN Inc.
www.tiltek.com
Superior Service
Steps in System Design
Using the previous worksheet, calculate the necessary fade margins and antenna gains at all CPE locations to guarantee link availability of approximately 99.995%.
Calculate the interference levels at each location from other systems to determine the amount of threshold degradation.
Select new antennas as necessary to compensate for degraded thresholds and maintain link availability and run the analysis again.
Repeat as necessary until all criteria for C/I and fade margin have been met.

## Slide 10
A Division of Wi-LAN Inc.
www.tiltek.com
Superior Service
Calculating Interference Between Two Antennas

## Slide 11
A Division of Wi-LAN Inc.
www.tiltek.com
Superior Service
For each antenna determine the gain, in dBi, in the direction to the other antenna.
For the antennas shown on the previous slide we have:
  Antenna #1: Gain at 135 degrees = (21 - 30) = -9.0 dBi.
  Antenna #2: Gain at 257 degrees = (21- 25) = -3.0 dBi.
  Assume:
    antennas are 10 km apart.
    10 m. LMR-400.
    Tx Power = 20 dBm.
  Using the link calculation worksheet we find:
    RSL = -119.56 dBm.
Calculating Interference Between Two Antennas

## Slide 12
A Division of Wi-LAN Inc.
www.tiltek.com
Affordable Quality
Initial System Configuration
Use omnidirectional antenna at the AP sites:
  Gain = 10 dBi
Choose the CPE antennas to provide enough or slightly more gain to provide the required fade margins.
Assume only one CPE is transmitting at any instant in time within any given AP “cell”.

## Slide 13
A Division of Wi-LAN Inc.
www.tiltek.com
Price – Performance Leader
Results of System Analysis
AP[1] may exhibit slightly degraded service.
AP[2] site has degraded service.
Two CPE sites are non-functional: [1,1] and [2,4].

## Slide 14
A Division of Wi-LAN Inc.
www.tiltek.com
Affordable Quality
Results of System Analysis

## Slide 15
A Division of Wi-LAN Inc.
www.tiltek.com
Solutions That Work
System Re-Design
Clearly the problem lies in the area around the path from CPE[2,4] through AP[2], AP[1] to CPE[1,1].
To solve the interference problems we propose to:
  Replace the omni at AP[1] with a combination of a sectoral antenna to provide a link to CPE[1,2], [1,3] and [1,4] and a directional point-to-point link from the AP to CPE[1,1].
  To provide additional isolation we will also use horizontal polarization for the point-to-point link to CPE[1,1].
  If necessary afterwards we will apply a similar approach at AP[2] to resolve any remaining marginal links.

## Slide 16
A Division of Wi-LAN Inc.
www.tiltek.com
Solutions That Work
System Re-Design (cont’d)
For the sectoral antenna we will choose a 120 degree sector.
  Although angle between CPE[1,2], AP[1] and CPE[1,4] is actually 122.9 degrees we can choose the CPE antennas as required.
For the point-to-point link we will use two 21 dBi directional antennas. This will ensure acceptable link availability while reducing interference to the AP[2] site. Furthermore, it allows us to choose the power divider required at AP[1] such that the sectoral links at this hub are acceptable.

## Slide 17
A Division of Wi-LAN Inc.
www.tiltek.com
Solutions That Work
System Re-Design (cont’d)

## Slide 18
A Division of Wi-LAN Inc.
www.tiltek.com
Price – Performance Leader
Results of New System Analysis
The problems from the initial design have been resolved.
We could still experience problems in the field due to unknown noise sources and additional interference. If possible, it is preferable to determine the strength and direction of sources of interference at the outset and factor this into the system design.

## Slide 19
A Division of Wi-LAN Inc.
www.tiltek.com
ISO 9001:94 Certified
Co-Locating systems on the same tower
Because it is often required, it is important to look at the particular issues in co-locating systems on the same tower or building site.
The most difficult problem to overcome is achieving the necessary isolation between systems.
Example
  Assume the same radio characteristics and transmission lines that we have been using throughout.
  Antenna #1: 21 dBi directional.
  Antenna #2: 24.5 dBi directional.
  How much isolation is required?
  How do we achieve it?
Even at a separation of more than 10 meters, it necessary to use cross-polarization to gain an additional 10-15 dB isolation.
  We assume only 10 dB discrimination since the direction of interference is well off the main beam and relative cross-polarization levels degrade.

## Slide 20
A Division of Wi-LAN Inc.
www.tiltek.com
Outstanding Reliability
Co-Locating systems on the same tower

## Slide 21
A Division of Wi-LAN Inc.
www.tiltek.com
Price – Performance Leader
Some Real Examples of Co-Located, Directional Antennas